## Slide 1: Chapter 2: Wireless Transmission
Frequency and signal
Channel and propagation
Multiplexing
Modulation

## Slide 2: Frequencies for communication
VLF = Very Low Frequency UHF = Ultra High Frequency
LF = Low Frequency SHF = Super High Frequency
MF = Medium Frequency EHF = Extra High Frequency
HF = High Frequency UV = Ultraviolet Light
VHF = Very High Frequency
1 Mm
300 Hz
10 km
30 kHz
100 m
3 MHz
1 m
300 MHz
10 mm
30 GHz
100 m
3 THz
1 m
300 THz
visible light
VLF
LF
MF
HF
VHF
UHF
SHF
EHF
infrared
UV
optical transmission
coax cable
twisted pair
FM Radio
AM Radio
mmWave (5G)

## Slide 3: Frequencies in use
VHF-/UHF-ranges for mobile radio
  simple, small antenna for cars
  Better propagation characteristics, relatively reliable connections
SHF and higher for directed radio links, satellite communication
  large bandwidth available
Wireless LANs use frequencies in UHF to SHF spectrum
  some systems planned up to EHF
  limitations due to absorption by water and oxygen molecules (shorter distance)
    weather dependent fading, signal loss caused by heavy rainfall, fog etc.

## Slide 4: Signal basics
Wireless signal is a physical representation of data
  A function of time and location
  Determined by parameters, which represent data
Signal classification
  continuous time/discrete time
  continuous values/discrete values
  analog signal =
  continuous time
  and continuous values
  digital signal
  discrete time and
  discrete values

## Slide 5: Radio waves
Radio waves are in fact E/M waves
  Electric and Magnetic fields
  Maxwell Equations demonstrated that variable E-field will generate a variable M-field, and vice versa.
Traverse
  meaning that such signals will actually travel through space, or vacuum without any medium.
Frequency, or rate of signal oscillation, f
  E-field and M-field will always have the same frequency.
  Any frequency is possible.
E
B

## Slide 6: Generation of radio waves
Radio wave generation can start from variable E-field in a dipole antenna.
T as signal period
T=1/f
t=0, E is at maximum value. Decreasing
t=T/4, E is at 0.
t=T/2, E is at negative maximum value.
t=3T/4, E is at 0.
t=T, E is at maximum value again.

## Slide 7: Propagation
The easiest way for radio waves to propagate is line-of-sight.
  Meaning that sender and receiver can see each other.
  And no barrier in between.
Reflection is also possible
  Similar to light
Role of the Ionosphere
100 MHz
1 MHz
10 MHz
Earth

## Slide 8: Wave propagation
Wireless signals propagate in a similar way as water waves
Starting from center
Slowly expands
By-passing larger objects with the help of water (media)
Reflection, etc.
Source: http://www.gemini.edu/

## Slide 9: Antennas: isotropic radiator
Radiation and reception of electromagnetic waves, coupling of wires to space for radio transmission
Isotropic radiator: equal radiation in all directions (three dimensional) - only a theoretical reference antenna
Real antennas always have directive effects (vertically and/or horizontally)
Radiation pattern: measurement of radiation around an antenna
z
y
x
z
y
x
ideal
isotropic
radiator

## Slide 10: Antennas: simple dipoles
Real antennas are not isotropic radiators but, e.g., dipoles with lengths /4 on car roofs or /2 as Hertzian dipole
  shape of antenna proportional to wavelength
Example: Radiation pattern of a simple Hertzian dipole
Antenna gain
  maximum power in the direction of the main lobe compared to the power of an isotropic radiator (with the same average power)
side view (xy-plane)
x
y
side view (yz-plane)
z
y
top view (xz-plane)
x
z
simple
dipole
/4
/2

## Slide 11: Antennas: directed and sectorized
side view (xy-plane)
x
y
side view (yz-plane)
z
y
top view (xz-plane)
x
z
top view, 3 sector
x
z
top view, 6 sector
x
z
Often used for microwave connections or base stations for mobile phones (e.g., radio coverage of a valley)
directed
antenna
sectorized
antenna

## Slide 12: Antenna: diversity
Grouping of 2 or more antennas
  multi-element antenna arrays
Antenna diversity
  switched diversity, selection diversity
    receiver chooses antenna with best signal
    sometimes dynamically
  diversity combining
    combine output power to produce gain
    phase-shifting needed to avoid cancellation
+
/4
/2
/4
ground plane
/2
/2
+
/2

## Slide 13: Signal propagation ranges
distance
sender
transmission
detection
interference
Transmission range
  communication possible
  low error rate
Detection range
  detection of the signal possible
  no communication possible
Interference range
  signal may not be detected
  signal adds to the background noise
Usually, RT < RD < RI

## Slide 14: Signal propagation, details
Propagation in free space always like light (straight line)
Receiving power proportional to 1/d²
  d = distance between sender and receiver (area of sphere surface)
Received signal power is also additionally influenced by
  fading (frequency dependent)
  shadowing
  reflection at large obstacles
  scattering at small obstacles
  diffraction at edges
reflection
scattering
diffraction
shadowing

## Slide 15: Multipath propagation
Signal can take many different paths between sender and receiver due to reflection, scattering, diffraction
Time dispersion: signal is dispersed over time
  interference with “neighbor” symbols, Inter Symbol Interference (ISI)
Signal reaches a receiver directly. So is a second (weaker) copy with phase shifted. Or a third.
  distorted signal depending on the phases of the different parts
signal at sender
signal at receiver

## Slide 16: Effects of mobility - fading
Channel characteristics change over time and location
  signal paths change
  different delay variations of different signal parts
  different phases of signal parts
quick changes in the power received (short-term fading)
Additional changes in
  distance to sender
  obstacles further away
 slow changes in the
average power received
(long-term fading)
short term fading
long term
fading
t
power

## Slide 17: Wavelength
Radio signals travel at speed of light
  c = 3*108 m/s
Frequency, f
  Defined as number of oscillations per second
Wavelength, 
  Defined as the distance between two points at the same phase
  c =  f
Higher frequency
 shorter wavelength

## Slide 18: Periodic signals
1
0
1
0
t
t
ideal periodic signal
real composition
(based on harmonics)
Sum of two
sine waves
Example of a signal:
s(t) = At sin(2  ft t + t)

## Slide 19: Sine wave parameters
Peak amplitude (A)
Frequency (f )
Period (T )
Phase ()
Wavelength ()
  maximum value or strength of the signal over time; typically measured in volts
  Rate, in cycles per second, or Hertz (Hz) at which the signal repeats
  amount of time it takes for one repetition of the signal (T = 1/f)
  measure of the relative position in time within a single period of a signal
  distance occupied by a single cycle of the signal
  Or, the distance between two points of corresponding phase of two consecutive cycles

## Slide 20: Example of signals
A=1
f=1Hz
 = 0
X-axis can be time or distance (space)

## Slide 21: Frequency-Domain Concepts
Frequency
  Just the number of signal repetitions in each second.
  Usually signals are not simple ones, but combination of different signals
Bandwidth
  The size (in frequency) of the signal from lowest frequency to highest frequency
Low-band filtering, high-band filtering, etc. can help with filtering those signals/noise that we don’t want.

## Slide 22: Representing datum in signals
Different representations of signals
  Deals with how to carry information
  Amplitude, frequency, phase representation
Composed signals can be transferred into frequency domain for better understanding
  using Fourier transformation
Digital signals have some special requirements:
  infinite number of frequencies for perfect transmission
  modulation with a carrier frequency for transmission that will make them analog signals for wireless transmissions.
f [Hz]
A [V]

I= M cos 
Q = M sin 

A [V]
t[s]

## Slide 23: Data Communication Terms
Data - entities that convey meaning, or information
Signals - electric or electromagnetic representations of data
Transmission - communication of data by the propagation and processing of signals
  In this course, we focus on delivery of data through wireless media/channels

## Slide 24: Examples of Analog and Digital Data
Analog
  Video
  Audio
Digital
  Text
  Integers

## Slide 25: Analog Signals
A continuously varying electromagnetic wave that may be propagated over a variety of media, depending on frequency
Examples of media:
  Copper wire media (twisted pair and coaxial cable)
  Fiber optic cable
  Atmosphere or space propagation
Analog signals can help propagate both analog and digital data

## Slide 26: Digital Signals
A sequence of voltage pulses that may be transmitted over a copper wire medium
Transmission generally easier than analog signaling
Less susceptible to noise interference
Suffer more from attenuation
Digital signals can help propagate both analog and digital data

## Slide 27: Analog Signaling

## Slide 28: Digital Signaling

## Slide 29: Different combinations
Digital data, digital signal
  Equipment for encoding is less expensive than digital-to-analog equipment
Analog data, digital signal
  Conversion permits use of modern digital transmission and switching equipment
Digital data, analog signal
  Some transmission media will only propagate analog signals
  Examples include optical fiber and satellite
Analog data, analog signal
  Analog data easily converted to analog signal

## Slide 30: Analog Transmission
Transmit analog signals without regard to content
Attenuation limits length of transmission link
Cascaded amplifiers boost signal’s energy for longer distances but can cause distortion
  Noise accumulates over distance
  Analog data can tolerate distortion
  Introduces errors in digital data

## Slide 31: Digital Transmission
Concerned with the content of the signal
Attenuation endangers integrity of data
Digital Signal
  Repeaters achieve greater distance
  Repeaters recover the signal and retransmit
Analog signal carrying digital data
  Retransmission device recovers the digital data from analog signal
  Generates new (and usually cleaner) analog signal

## Slide 32: Chapter outline
Frequency and signal
Channel and propagation
Multiplexing
Modulation

## Slide 33: Channel capacity
Impairments, such as noise, limit data rate that can be achieved
For digital data, to what extent do impairments limit data rate?
  Data rate: the number of bits sent/received successfully
Channel Capacity
  the maximum rate at which data can be transmitted over a given communication path, or channel, under given conditions
  Note that a different condition will lead to different channel capacity.

## Slide 34: Concepts Related to Channel Capacity
Channel bandwidth - the bandwidth of the transmitted signal as constrained by the transmitter and the nature of the transmission medium (in Hertz, Hz)
Noise - average level of noise over the communication path
Error rate - rate at which errors occur
  Error = transmit 1 and receive 0; transmit 0 and receive 1
  E.g., sent 1011 and received 1001, 1/4=25% error rate.
  0.1% error rate means that 1 error per 1Kbits data
Energy level of signal also plays an important role, thus…

## Slide 35: Signal-to-Noise Ratio
Ratio of the power in a signal to the power contained in the noise that’s present at a particular point in the transmission
Typically measured at a receiver
Signal power to noise power ratio (SNR, or S/N)
A high SNR usually represents a high-quality signal.
  Fewer repeaters needed.
SNR sets upper bound on achievable data rate (or channel capacity)

## Slide 36: dB, dBW, and dBm
dB is a ratio, converted to logarithm
  For example, ratio of r=100
  Converted to dB = 10log10 (100) = 20 dB
dBW is a power unit, in relation to Watt
  The transmission of a signal is 1000 Watt
  Or 10log10 (1000W/1W) = 30 dBW
dBm is also a power unit, in relation to mW
  The transmission of a signal is 0.01 mW
  Or 10log10 (0.01mW/1mW) = -20 dBm

## Slide 37: Shannon Capacity Formula
Equation:
Represents theoretical maximum that can be achieved
  Upper bound of achievable data rate
In practice, only much lower rates achieved
  Formula assumes white noise (thermal noise)
  Impulse noise is not accounted for
  Attenuation distortion or delay distortion not accounted for

## Slide 38: Example
Spectrum of a channel between 3 MHz and 4 MHz ; SNRdB = 24 dB
Using Shannon’s formula

## Slide 39: Chapter outline
Frequency and signal
Channel and propagation
Multiplexing
Modulation

## Slide 40: Multiplexing
Multiplexing in 4 dimensions
  space (s)
  time (t)
  frequency (f)
  code (c)
Goal: multiple users for a shared medium
Important: guard spaces needed!
s2
s3
s1
f
t
c
k2
k3
k4
k5
k6
k1
f
t
c
f
t
c
channels ki

## Slide 41: Frequency multiplex
Spectrum separation
  Spectrum separated into smaller bands
  Each channel/user gets one band/frequency
Advantages:
  no dynamic coordination necessary
  Also works for analog signals
Disadvantages:
  waste of bandwidth if the traffic is distributed unevenly
  Not flexible enough
  guard spaces
k2
k3
k4
k5
k6
k1
f
t
c

## Slide 42: Time multiplex
f
t
c
k2
k3
k4
k5
k6
k1
A channel gets the whole spectrum for a certain amount of time
Advantages:
  only one carrier in the medium at any time
  Achieves high throughput even with many users
Disadvantages:
  Precise time
  synchronization necessary

## Slide 43: Time and frequency multiplex
f
Combination of both methods
  A channel gets a certain frequency band for a certain time
Advantages:
  better protection against tapping
  protection against frequency selective interference
  higher data rates compared to code multiplex (next)
Issues
  precise coordination required
t
c
k2
k3
k4
k5
k6
k1

## Slide 44: Code multiplex
Each channel has a unique code
  All channels use the same spectrum at the same time
Advantages:
  bandwidth efficient
  no coordination and synchronization necessary
  good protection against interference and tapping
Disadvantages:
  lower user data rates
  more complex signal regeneration
Implemented using spread spectrum technology
k2
k3
k4
k5
k6
k1
f
t
c

## Slide 45: Chapter outline
Frequency and signal
Channel and propagation
Multiplexing
Modulation

## Slide 46: Modulation
Digital modulation
  digital data is translated into an analog signal (baseband)
  ASK, FSK, PSK - main focus in this chapter
  differences in spectral efficiency, power efficiency, robustness
Analog modulation
  shifts center frequency of baseband signal up to the radio carrier
Motivation
  smaller antennas (e.g., /4)
  Frequency Division Multiplexing
  medium characteristics

## Slide 47: Modulation and demodulation
synchronization
decision
digital
data
analog
demodulation
radio
carrier
analog
baseband
signal
101101001
radio receiver
digital
modulation
digital
data
analog
modulation
radio
carrier
analog
baseband
signal
101101001
radio transmitter
Your cable modem is doing essentially the same thing.

## Slide 48: Digital modulation
Modulation of digital signals known as Shift Keying
Amplitude Shift Keying (ASK):
  very simple
  low bandwidth requirements
  very susceptible to interference
Frequency Shift Keying (FSK):
  needs larger bandwidth
Phase Shift Keying (PSK):
  more complex
  robust against interference
1
0
1
t
1
0
1
t
1
0
1
t

## Slide 49: Advanced Phase Shift Keying
BPSK (Binary Phase Shift Keying):
  bit value 0: sine wave
  bit value 1: inverted sine wave
  very simple PSK
  low spectral efficiency
  robust, used e.g. in satellite systems
QPSK (Quadrature Phase Shift Keying):
  2 bits coded as one symbol
  symbol determines shift of sine wave
  needs less bandwidth compared to BPSK
  more complex
DQPSK - Differential QPSK
  0010,1101  compute the differential bits
  0011,1011
Q
I
0
1
Q
I
11
01
10
00

## Slide 50: Quadrature Amplitude Modulation
Quadrature Amplitude Modulation (QAM): combines amplitude and phase modulation
it is possible to code n bits using one symbol
2n discrete levels, n=2 identical to QPSK
bit error rate increases with n
0000
0001
0011
1000
Q
I
0010
  16-QAM (4 bits = 1 symbol)
Symbols 0011 and 0001 have the same phase, but different amplitude. 0000 and 1000 have different phase, but same amplitude. used in standard 9600 bit/s modems