## Slide 1: Chapter 5. Wireless Sensor Networks

## Slide 2: Outline
Sensor Hardware
Constraints
Design Factors
Protocol Stacks
Applications

## Slide 3: Wireless Sensor Networks
WSNs are composed of a large number of sensor nodes, which are densely deployed either inside the phenomenon or very close to it.
Sensors
Networking, data processing techniques
Communication medium

## Slide 4: Sensor Hardware
StarGate (Intel X-Scale 400-MHz CPU)
MK-II (UCLA medusa, COTS-based)
iBadge (UCLA)
MICA Mote

## Slide 5: Berkeley’s Motes
COTS dust prototypes
weC Motes (light, temp)
Rene Stack
MicaZ node (250kbps, router)

## Slide 6: Telos Rev. B (new Mote)
Single board philosophy
  Easy to use, low cost
  Sensing humidity, temperature, light
250 kbps, 2.4 GHz
IEEE 802.15.4, ZigBee-ready
Quick wakeup
  <6 usec

## Slide 7: Mica weather board
Photosynthetically active radiation
  Formation of carbohydrates
Relative humidity
  ±2%
Barometric Pressure
  ±1.5mbar
Temperature
  ±0.01C

## Slide 8: Other Sensor Boards
Ultrasonic transceiver – Localization
  Used for ranging
  Up to 2.5m range
  0.06m accuracy
  Dedicated uPU
  25 kHz element
Basic Sensor board
  Light (photo)
  Temperature
  Acceleration
  Magnetometer
  Microphone, tone
  Detector, Sound

## Slide 9: Berkeley Dust Mote

## Slide 10: Outline
Sensor Hardware
Constraints
Design Factors
Protocol Stacks
Applications

## Slide 11: Constraints of Sensors
Un-tethered
  No tethered power, wireless
Cost
  Large-scale, dense deployment
  Cheaper manufacturing
Physical size
  Fit into almost everywhere
Lifetime
  Change of battery un-economic

## Slide 12: Constraints (cont’d)
Which of the following constraints may really matter in 5-10 years from now?
Energy limitations
Design/deployment for dense networks
Dynamic radio communication environment
Large multi-hop networks
Processor speed
Memory size

## Slide 13: Energy Sources
 | Available power
Battery (Zinc-Air) | 1050-1560 mWh/cm3
Battery (Lithium ion) | 300 mWh/cm3
Solar (outdoors) | 0.15-15 mW/cm2
Solar (indoors) | .006 mW/cm2
Vibrations | 0.001-0.1 mW/cm3
Acoustic Noise | 3 pWh/cm2 at 75dB
Passive Human Powered | 1.8 mW (shoe inserts)
Thermal conversion | 0.002 mW ~ 5 degrees
Fuel Cells | 500 mWh/cm3

## Slide 14: Communication vs. Computation costs
 | 1999 (Bluetooth) | 2004
Communication | 150 nJ/bit 1.5 mW | 5 nJ/bit 0.05 nW
Computation |  | 100 GOPS/W 10 pJ/OP
10 kbps, 10-meter radio range
Cost of communication is un-proportionally larger than cost of computation

## Slide 15: WSNs vs. Traditional Distributed Systems
Energy as major constraint
  Turning off unused devices
Other constraints
  Memory, computation, bandwidth
Self-organized, autonomous systems
  Address-free, no global names
Correlated data
  Unique correlation of local data in WSNs
  In-network processing possible
Single destination

## Slide 16: WSNs vs. Ad hoc Networks
More nodes
  several orders of magnitude higher
Sensor nodes are densely deployed
Sensor nodes are prone to failures
Some WSNs’ topology may change frequently
Communication mechanisms
  Broadcast vs. peer-2-peer
Sensor nodes are limited in power, computational capacities and memory.
Sensor nodes may not have global ID.

## Slide 17: Outline
Sensor Hardware
Constraints
Design Factors
Protocol Stacks
Applications

## Slide 18: System Design Themes
Long-lived systems
  Un-tethered, un-attended
  Communication as major consumer of scarce energy
  Autonomy requires robust, adaptive, self-configuring systems
Leverage data processing inside WSNs
  Exploit computations near data, achieving scalability
  Collaborative signal processing
  Achieve desired global behavior with localized algorithms – distributed control
“The Network is the sensor”

## Slide 19: Design factors: fault tolerance
Fault tolerance is the ability to sustain sensor network functionalities without any interruption due to sensor node failures.
The fault tolerance level depends on the application of the sensor networks.
Probability of no failures: Rk(t)=e-kt

## Slide 20: Design factors: scalability
Scalability measures the density of the sensor nodes.
How many nodes in a local area.
Random distribution, N sensors in area of size A.
Density: (R) =(NR2)/A

## Slide 21: Design factors: production cost
Cost of a single node
  Should justify the overall cost of the networks
Huge amount of functionalities:
  Battery, CPU, memory, sensor, tx-rx…
  A price of much less than a dollar

## Slide 22: Design factors: hardware constraints

## Slide 23: Design factors: network topology
Pre-deployment and deployment phase
  Dropped off from planes
  Or placed one-by-one
Post-deployment phase
  Mobility or failure
Re-deployment
  Additional nodes

## Slide 24: Design factors: environment
Close to or inside the phenomenon of observation
Interior of large machinery
Bottom of an ocean
Biologically/chemically contaminated field
Battlefield
Home or building

## Slide 25: Design factors: transmission media
Potential media
  Radio (2.4 GHz, 891 MHz)
  Infrared
  Optical media
Multi-hop networks are formed

## Slide 26: Design factors: power consumption
Limited reserve, hard to refill
Sensing
  Do we always need to turn every node on?
Communication
  Shrink the tx-range
Data processing
  Process before transmission

## Slide 27: Outline
Sensor Hardware
Constraints
Design Factors
Protocol Stacks
Applications

## Slide 28: Protocol stack
Power Management
  How to use its power
Mobility Management
  Detecting movements
Task Management
  Scheduling sensing tasks

## Slide 29: Physical layer
Frequency selection
Carrier frequency generation
Signal detection
Modulation
Encryption
Receiver side

## Slide 30: Physical layer: research issues
Modulation schemes
Strategies to overcome signal propagation effects
Hardware design
Optimize the transmission power of each sensor

## Slide 31: Data link layer
Medium access control
Error control
Ensuring connections
  point-to-point
  point-to-multipoint

## Slide 32: Data link layer: Medium access control (MAC)
Establish communication links
Share communication resources
  Efficiency
  Fairness
  Conserve energy
New MAC techniques are needed

## Slide 33: Data link layer: error control
Forward Error Correction (FEC)
  Parity-check, e.g.
  Encoding and decoding consume power
Automatic Repeat reQuest (ARQ)
  Multi-hop retransmissions?
BER, SNR, Es/N0

## Slide 34: Data link layer: research issues
MAC for mobile sensor networks
Determination of lower bounds on the energy required for sensor network self-organization
Error control coding schemes.
Power saving modes of operation

## Slide 35: Network layer
Multi-hop networking protocols needed
  As compared to Wireless LAN
  Large number of hops away from sink
Several considerations:
  Power efficiency
  Data centric
  Data aggregation
  Attribute-based addressing and location awareness

## Slide 36: Network layer: route selections
Route 1: sink-A-B-T, PA=4, α=3
Route 2: sink-A-B-C-T, PA=6, α=6
Route 3: sink-D-T, PA=3, α=4
Route 4: sink-E-F-T, PA=5, α=6
Minimum energy: route 1
Minimum hop: route 3
Maximum available power (PA): route 2
Maximum minimum PA node: route 3
Others?

## Slide 37: Network layer: data aggregation
Works like a reversed broadcast tree
Node E combines data from A and B
Node G does the same
Reduction of transmissions

## Slide 38: Data fusion
Large amount of data for the end user
Need methods of combining or aggregating data into small set of information
  Energy saving
Data aggregation (aka data fusion) can combine unreliable data readings to produce accurate signal
  improving the common signal
  reducing the noise

## Slide 39: LEACH
LEACH (Low-Energy Adaptive Clustering Hierarchy)
  A clustering-based protocol
  Utilizes the randomized rotation of local cluster base stations
  Evenly distribute the energy load within the network of sensors
Distributed, no need for knowledge of global network for LEACH to function

## Slide 40: LEACH: energy saving
The energy saving of LEACH is achieved by combining compression with data routing
Key features of LEACH include:
Localized coordination and control of cluster set-up and operation
Randomized rotation of the cluster base stations or clusterheads and their clusters
Local compression of information to reduce global communication

## Slide 41: LEACH: assumptions
The base station is fixed and located far from the sensors
All the sensor nodes are homogeneous and energy constrained
Communication between sensor nodes and the base station is expensive and no high energy nodes exist to achieve communication

## Slide 42: LEACH: strategies
Only CH’s are sending to BS
Rotating CH’s to avoid draining one sensor’s energy
Local compression is also used to reduce transmission

## Slide 43: LEACH: CH selection
  The node (n) decides by choosing a random number between 0 and 1
  If this random number is less than T(n), the nodes become a CH for this round
  The threshold is set as follows:

## Slide 44: LEACH: cluster formation
CH advertisement phase
Cluster set-up phase
  the non-CH nodes hear the ads of all CHs and decide which CH to join
  A node joins to a CH in which it hears with its advertisement with the highest signal strength
Upon receiving all the join messages from its members, CH creates a TDMA schedule about their allowed transmission time based on the total number of members in the cluster

## Slide 45: LEACH: data transmission
Each node starts data transmission to their CH based on their TDMA schedule
The radio of each cluster member nodes can be turned OFF until their allocated transmission time comes; minimizing the energy dissipation
The CH nodes must keep its receiver ON to receive all the data
Once all the data is received, the CH compresses the data to send it to BS

## Slide 46: LEACH: multiple clusters
In order to minimize the radio interference between nearby clusters, each CH chooses randomly from a list of spreading CDMA codes and it informs its cluster members to transmit using this code.
The neighboring CHs radio signals will be filtered out to avoid corruption in the transmission.
Redundant clusters can be eliminated as well.

## Slide 47: LEACH: advantages
Localized coordination to enable scalability, and robustness for dynamic networks
Incorporates data fusion into the routing protocol in order to reduce the amount of information transmitted to BS
Distributes energy dissipation evenly throughout the sensors, thus increasing the system lifetime of the network

## Slide 48: LEACH: disadvantages
How to decide the percentage of cluster heads for a network? The topology, density and number of nodes of a network could be different from other networks
No suggestions about when the re-election needs to be invoked
The CH’s farther away from the base station will use higher power and die more quickly than the nearby ones.

## Slide 49: SPIN: information dissemination
SPIN (Sensor Protocols for Information via Negotiation) is a negotiation-based information dissemination protocols.
  Addressing the deficiencies of classic flooding problem
  With negotiation and resource-adaptation
SPIN disseminates information
  From each sensor
  To all sensors
  Treating all sensors as potential sink nodes

## Slide 50: SPIN: meta-data
Nodes using SPIN protocols names their data using high-level data descriptors, called meta-data
  Usage of meta-data negotiations is efficient
  Eliminate transmission of redundant data in the network
Communication decisions can be based upon
  Application-specific knowledge of the data
  Knowledge of the resources available to nodes

## Slide 51: SPIN: basic ideas
Operate efficiently and conserve energy
  communicate with each other about the sensor data received already and the data needed still
Monitor and adapt changes in their own energy resources: extend the lifetime of the system
Four difference SPIN protocols:
  SPIN-PP
  SPIN-EC
  SPIN-BC
  SPIN-RL

## Slide 52: SPIN: meta-data requirements
Used to uniquely and completely describe the data being collected by sensors
If two pieces of actual data are distinguishable, then their meta-data should also be distinguishable
Since the format of meta-data is application-specific, each application needs to interpret and synthesize its own meta-data
  ADV (new data advertisement)
  REQ (request for data)
  DATA (data message)

## Slide 53: SPIN: problem statement
Problems with conventional classic flooding
  The source nodes sends data to all its neighbors and the neighbors check their record of already sent data to see if they have forwarded the data to their neighbors.
  If not, they forward the data and update the record
This requires small amount of protocol state at any node, disseminates data quickly in the network
Three main issues:
  Implosion - A node always sends data to its neighbors without being concerned about if the same data has been received by the neighbors from other nodes
  Overlap
  Resource blindness

## Slide 54: SPIN: methods
Nodes negotiating with each other before transmitting data eliminates the transmission of redundant data
Nodes poll their resources before transmitting or processing data by probing the resource manager which keeps track of the resource consumption
Nodes can make efficient decisions based on the available energy level
Eliminates the possibility of overlap since the nodes can name the part of the data the nodes are interested in receiving
Resource-awareness of local resources allow sensors to make meaningful decisions to extend longevity

## Slide 55: SPIN-PP
SPIN-PP works in three stages (ADV-REQ-DATA)
  each stage corresponding to one of the messages
The node sends ADV message to its neighbors
Neighbors check to see if they already have received or requested this data
If not, the neighbors respond by sending REQ message to the sender
The sender responds to the REQ message sent by sending the actual DATA to the neighbors requesting the data
Silence otherwise.

## Slide 56: SPIN-EC
Adds simple energy-conservation heuristic to the SPIN-PP protocol
  When energy is abundant, SPIN-EC acts as SPIN-PP protocol
  Whenever energy comes close to low-energy threshold, it adapts by reducing its participation
It does not prevent nodes from receiving messages such as ADV or REQ below its low-energy threshold, but prevents the nodes to handle a DATA message below the threshold

## Slide 57: Directed Diffusion
data-centric approach
Data generated by sensor nodes is named using attribute-value pairs
A node requests data by sending interests for named data
Nodes diffusing the interest sets up their own caches and gradients within the network to which channel the delivery of data
During the data transmission, reinforcement and negative reinforcement are used to converge to efficient distribution

## Slide 58: Directed Diffusion: interest
Interest is generally given by the sink node
Periodical broadcast of interest with monotonically increasing timestamp attribute for reliability purposes

## Slide 59: Directed Diffusion: gradient
The interest entry contains several gradient fields, up to one per neighbor
This entry has single gradient towards the neighbor
  from which the interest was received with specified data rate
Individual neighbors can be distinguished by locally unique identifiers

## Slide 60: Directed Diffusion: data
Data message is unicast individually to the relevant neighbors
A node receiving a data message from its neighbors checks to see if matching interest entry in its cache exists according the matching rules described
Forwarded
Reinforcement phase

## Slide 61: Directed Diffusion: advantages
Data-centric dissemination
Robust multi-path delivery
Reinforcement-based adaptation to the empirically best network path
Energy savings with in-network data aggregation and caching
Gives designers the freedom to attach different semantics to gradient values
Reinforcement can be triggered not only by sources but also by intermediate nodes

## Slide 62: Three papers
[Heinzelman+ 2002] W. Heinzelman, A.P. Chandrakasan and H. Balakrishnan, An Application-Specific Protocol Architecture for Wireless Microsensor Networks, IEEE Transactions on Wireless Communications, Vol. 1, No. 4, October 2002, pp. 660-670.
[Intanagonwiwat + 2000] C. Intanagonwiwat, R. Govindan and D. Estrin, Directed Diffusion: A Scalable and Robust Communication Paradigm for Sensor Networks, In Proceedings of the Sixth Annual International Conference on Mobile Computing and Networks (MobiCOM 2000), August 2000, Boston, Massachusetts
[Kulik+ 2002] J. Kulik, W. Heinzelman and H. Balakrishnan, Negotiation-Based Protocols for Disseminating Information in Wireless Sensor Networks, Wireless Networks 8, 2002, pp. 169-185.

## Slide 63: Transport layer
Needed for inter-connection with Internet or other external networks.
Little work been done:
  Address-free
  Data centric communication
  “Show me the area with temperature higher than 80F”
New protocol needed

## Slide 64: Application layer
Interface between user software and lower layer functionalities
Sensor management protocol (SMP)
  Sensor control, authentication, etc.
Task assignment and data advertisement protocol (TADAP)
  Task control
Sensor query and data dissemination protocol (SQDDP)
  Information dissemination

## Slide 65: Outline
Sensor Hardware
Constraints
Design Factors
Protocol Stacks
Applications

## Slide 66: WSN example

## Slide 67: What can be sensed?
temperature
humidity
vehicular movement
lightning condition
pressure
soil makeup
noise levels
the presence or absence of certain kinds of objects
mechanical stress levels on attached objects
the current characteristics such as speed, direction, and size of an object

## Slide 68: Military applications
Monitoring friendly forces, equipment and ammunition
Battlefield surveillance
Reconnaissance of opposing forces and terrain
Battle damage assessment
Nuclear, biological and chemical attack detection and reconnaissance

## Slide 69: Environmental applications
Forest fire detection
Wild animal spotting and tracking
Biosphere monitoring
Flood detection
Precision agriculture

## Slide 70: Health application
Smart clothing
Patient monitoring
  early-warning system
Tracking and monitoring patients and doctors inside a hospital
Drug administration in hospitals

## Slide 71: Home applications
Home security
Home automation
Smart environment
Internet-of-Things (IoT)
  Devices usually directly connected to Internet

## Slide 72: Commercial applications
Inventory control
Fleet vehicle tracking and control
Smart road
  “stay-in-your-lane”
  Speed control
  Congestion avoidance
Interactive museums