## Slide 1: Chapter 6: Spread Spectrum and Error Coding

## Slide 2: Spread Spectrum
Communication: input is fed into a channel encoder
  Produces analog signal with narrow bandwidth
    Information-rich content requires wider bandwidth.
  In traditional systems, this bandwidth does not change at all even though it can be moved to higher frequency for transmission (carrier).
Spread Spectrum: signal is further modulated using sequence of digits
  Spreading code or spreading sequence, with special properties
Effect of modulation is to increase bandwidth of signal to be transmitted
  With benefits

## Slide 3: Model and benefits
Digit sequence is used to demodulate the spread spectrum signal
By feeding the received signal into a channel decoder with the same pseudorandom code/sequence
Immunity from various kinds of noise and multipath distortion
Can be used for hiding and encrypting signals
Several users can independently use the same wider bandwidth with very little interference (orthogonality)

## Slide 4: Illustration of spreading
Signal bandwidth (blue line)
  Bs
After spectrum spreading (red line)
  Bc
Signal is now hidden in noise!
Shorter pulse -> higher frequency

## Slide 5: Reception of de-spreading
Receiver gets a combination of
  Black line
  Red line
  Cyan line
After de-spreading
  Red line becomes blue line (this is what we need)
  Black line remains
  Cyan line takes the form of red line!
A band-pass filter will screen most of the noise and interference.
Spike interference

## Slide 6: Direct Sequence Spread Spectrum
Two categories of spread spectrum
  Direct Sequence Spread Spectrum (DSSS)
  Frequency Hopping Spread Spectrum (FHSS)
Each bit in original signal is represented by multiple bits in the transmitted signal
Spreading code spreads signal across a wider frequency band
  Spread is in direct proportion to number of bits used
One technique combines digital information stream with the spreading code bit stream using exclusive-OR
XOR - Exclusive OR
  Returning 1 only when the two inputs are different.
  a XOR 1 = ~a
  a XOR 0 = a
  a XOR a = 0
  (a XOR b) XOR c = a XOR (b XOR c)

## Slide 7: Bit Sequence XOR
It can be proven that A’=A
Synchronization of PN bit stream
A
B
C
C
B
A’

## Slide 8: DSSS Using BPSK
Multiply BPSK signal,
  sd(t) = A d(t) cos(2 fct)
by c(t) [takes values +1, -1]:
  s(t) = A d(t)c(t) cos(2 fct)
  A = amplitude of signal
  fc = carrier frequency
  d(t) = discrete function [+1, -1]
At receiver, incoming signal multiplied by c(t)
  c(t)•c(t) = Constant (we can treat it as 1)
  Incoming signal is then recovered

## Slide 9: Code-Division Multiple Access (CDMA)
Different codes for different users
  D = rate of data signal
  Break each bit into k chips
    Chips are a user-specific fixed pattern
  Chip data rate of new channel = kD
If k=6 and code is a sequence of 1s and -1s
  For a ‘1’ bit, A sends code as chip pattern
    <c1, c2, c3, c4, c5, c6>
  For a ‘0’ bit, A sends complement of code
    <-c1, -c2, -c3, -c4, -c5, -c6>
Receiver knows sender’s code and performs electronic decode function
    <d1, d2, d3, d4, d5, d6> = received chip pattern
    <c1, c2, c3, c4, c5, c6> = sender’s code

## Slide 10: CDMA Example
User A’s code = <1, –1, –1, 1, –1, 1>
  To send a 1 bit = <1, –1, –1, 1, –1, 1>
  To send a 0 bit = <–1, 1, 1, –1, 1, –1>
User B’s code = <1, 1, –1, – 1, 1, 1>
  To send a 1 bit = <1, 1, –1, –1, 1, 1>
Receiver receiving with A’s code
  (A’s code) x (received chip pattern)
    User A ‘1’ bit: 6 -> 1
    User A ‘0’ bit: -6 -> 0
    User B ‘1’ bit: 0 -> unwanted signal, ignored

## Slide 11: Codes of Three Users

## Slide 12: Codes of Three Users

## Slide 13: CDMA for DSSS
Ignoring attenuations and multipath reception

## Slide 14: Orthogonal Codes
ci(t) and cj(t) should be orthogonal to each other (when i≠j)
Example:
  (+1, +1, -1, -1, +1, +1)
  (-1, +1, -1, +1, +1, -1)

## Slide 15: Typical Multiple Spreading Approach
Spread data rate by an orthogonal code (channelization code)
  Provides mutual orthogonality among all users in the same cell
Further spread result by a PN sequence (scrambling code)
  Provides mutual randomness (low cross correlation) between users in different cells

## Slide 16: Frequency Hopping Spread Spectrum
Signal is broadcast over seemingly random series of radio frequencies
  A number of channels allocated for the FH signal
  Width of each channel corresponds to bandwidth of input signal
Signal hops from frequency to frequency at fixed intervals
  Transmitter operates in one channel at a time
  Bits are transmitted using some encoding scheme
  At each successive interval, a new carrier frequency is selected

## Slide 17: Hopping among frequencies
Channel sequence dictated by spreading code
Receiver hops between frequencies in synchronization with transmitter
  Eavesdroppers hear only unintelligible blips
  Attempts to jam signal on one frequency succeed only at knocking out a few bits

## Slide 18: FHSS Using MFSK
MFSK signal is translated to a new frequency every Tc seconds by modulating the MFSK signal with the FHSS carrier signal
For data rate of R:
  duration of a bit: T = 1/R seconds
  duration of signal element: Ts = LT seconds
Tc  Ts - slow-frequency-hop spread spectrum
Tc < Ts - fast-frequency-hop spread spectrum

## Slide 19: Coping with Data Transmission Errors
Error detection codes
  Detects the presence of an error
Automatic repeat request (ARQ) protocols
  Discarding the block of data with error(s).
  Sender retransmits same block
Error correction codes, or forward correction codes (FEC)
  Designed to detect and correct errors
Wireless transmissions can experience many errors.
  Need to cope with such errors

## Slide 20: Error Probability
Pb : Probability of single bit error (BER)
P0 : Probability that a frame arrives with no bit errors
P1 : Probability of 1-bit error
Pe: While using error detection (capable of detecting 1-bit error), the probability that a frame arrives with undetected errors
F: number of bits per frame
Example
Pb=10-6, F=1000
P0=(1-10-6)1000≈0.999
P1=0.0009995
Pe=5x10-7
i.i.d. error
occurrence

## Slide 21: Error Detection Process
Transmitter
  For a given frame, an error-detecting code (check bits) is calculated from data bits
  Check bits are appended to data bits and both are transmitted
Receiver
  Separates incoming frame into data bits and check bits
  Calculates check bits from received data bits
    Computation algorithm known to both
  Compares calculated check bits against received check bits
  Error detected if mismatch

## Slide 22: Illustration
Error can occur in data or check bits;
so this leads to wrong decisions

## Slide 23: Error Detection Techniques
Parity Check
Cyclic Redundancy Check
  Modulo 2 Arithmetic
  Polynomials
  Digital logic (hardware implementation)
We will discuss each of these in this chapter.

## Slide 24: Parity Check
Parity bit appended to a block of data
  Detection of errors with odd number of bits
Even parity
  Added bit ensures an even number of 1s
Odd parity
  Added bit ensures an odd number of 1s
Example, 7-bit character [1110,001]
  Even parity [1110,0010]
  Odd parity [1110,0011]

## Slide 25: Parity Check Examples
Example, 7-bit character [1110,001]
  Even parity [1110,0010]
It can be proven that, if only one bit is received incorrectly, the error will be detected:
  [1111,0010]
  Even parity will detect the error, although the error bit could be at the parity bit location.
    [1110,0011]
Only detection is possible, parity check can’t tell which bit is wrong.
  E.g., even parity check receiving [1011,0101]

## Slide 26: Cyclic Redundancy Check (CRC)
Transmitter
  For a k-bit block, transmitter generates an (n-k)-bit frame check sequence (FCS)
  Resulting frame of n bits is exactly divisible by predetermined number
Receiver
  Divides incoming frame by predetermined number
  If remainder is 0, assumes no error

## Slide 27: CRC using Modulo 2 Arithmetic (XOR)
Input: D; Output: F
Goal: T=(D || F)/P
has a remainder of 0
Procedure:
  Divide 2n-kD by P: quotient and remainder (R)
  F <- R
D
F
T
k bits
n-k bits
P
Pattern (divisor, n-k+1 bits)
T = n-bit frame to be transmitted
D = k-bit block of data; the first k bits of T
F = (n – k)-bit FCS; the last (n – k) bits of T
P = pattern of n–k+1 bits (predetermined divisor)
Q = Quotient
R = Remainder

## Slide 28: Proof of zero remainder
Remainder of T/P
Substituting,
  R+R = R XOR R = 0
  No remainder, so T is divisible by P

## Slide 29: Example of CRC using XOR
D=1010001101
P=110101
F=R=01110
(n,k)
n=15, k=10, n-k=5
All calculations in XOR

## Slide 30: CRC using Polynomials
All values expressed as polynomials
  Dummy variable X with binary coefficients
  The binary coefficients of the polynomials can represent binary numbers:
    X3 +X +1 is equivalent to
    1 0 1 1

## Slide 31: Some P(X) Functions
P(X) needs to be indivisible to demonstrate some good properties for CRC.
Widely used versions of P(X)
  CRC–12
    X12 + X11 + X3 + X2 + X + 1
  CRC–16
    X16 + X15 + X2 + 1
  CRC – CCITT
    X16 + X12 + X5 + 1
  CRC – 32
    X32 + X26 + X23 + X22 + X16 + X12 + X11 + X10 + X8 + X7 + X5 + X4 + X2 + X + 1

## Slide 32: Indivisible P(x)
How to check whether a polynomial is indivisible then?
Definition of indivisible
  There exists no other polynomials g(x) and h(x) such that f(x) = g(x) * h(x)
Checking indivisible
  Find all indivisible polynomials with degree lower than ceil(D(f(x))/2)
  Question: why don’t we need to check other polynomials?

## Slide 33: Error Detection not Enough
Error detection requires retransmission
  Appropriate in wire-line transmission with low error rate (~10-9)
However, in wireless applications
  error rate on wireless link can be high (~10-3), resulting in a large number of retransmissions
  long propagation delay compared to transmission time (satellites)
One step further,
error correction after detection.

## Slide 34: Block Error Correction Codes
Transmitter
  Forward error correction (FEC) encoder maps each k-bit block into an n-bit block codeword
  Codeword is transmitted over wireless channel
Receiver
  Each block is passed through an FEC decoder
  Up to a certain number of errors can be corrected

## Slide 35: Block Diagram

## Slide 36: Four Possible Results
No errors; no error detected
  Codeword produced by decoder matches original codeword
Errors; detected and corrected
Errors; detected but uncorrected
Errors; undetected (and uncorrected)
Number of error bits increases

## Slide 37: Block Code Principles
Hamming distance – for 2 n-bit binary sequences, the number of different bits
  E.g., v1=011011; v2=110001; d(v1, v2)=3
Redundancy – ratio of redundant bits to data bits
Code rate – ratio of data bits to total bits
Coding gain – the reduction in the required Eb/N0 to achieve a specified BER of an error-correcting coded system

## Slide 38: Hamming Distance
Imagine a code space
  where the distance between any two points is measured as Hamming distance
Some codewords (points) are good choices
00000
11100
11110
11001
00111
01110
h=3
Assuming that red code words are used,
now 11100 is received. What has been sent?

## Slide 39: Number of Correctable Errors
Minimum distance between any pair of codes
Number of correctable errors, t
wi
wj
dmin=5 or 6

## Slide 40: Hamming Code
Designed by Richard Hamming to correct single bit error
Family of (n, k) block error-correcting codes with parameters:
  Block length: n = 2m – 1
  Number of data bits: k = 2m – m – 1
  Number of check bits: n – k = m
  Minimum distance: dmin = 3
The above code is also an SEC-DED code:
  Single-error-correcting (SEC) code
  Double-error-detecting (DED) code

## Slide 41: Hamming Code Process
Encoding: k data bits + (n -k) check bits
Decoding: compares received (n -k) bits with calculated (n -k) bits using XOR
  Resulting (n -k) bits called syndrome word
  Syndrome range is between 0 and 2(n-k)-1
Example:
  k=7, n=10, m=3
  Syndrome word can pinpoint 23-1=7 different errors.
    000 -> no error
    001 -> first bit was wrong
    …
    111 -> seventh bit was wrong

## Slide 42: Cyclic Codes
Can be encoded and decoded using linear feedback shift registers (LFSRs)
For cyclic codes, a valid codeword (c0, c1, …, cn-1), shifted right one bit, is also a valid codeword (cn-1, c0, …, cn-2)
Takes fixed-length input (k) and produces fixed-length check code (n-k)
  In contrast, CRC error-detecting code accepts arbitrary length input for fixed-length check code

## Slide 43: BCH Codes
For positive pair of integers m and t, a (n, k) BCH code has parameters:
  Block length: n = 2m – 1
  Number of check bits: n – k ≤ mt
  Minimum distance:dmin ≥ 2t + 1
Correct combinations of t or fewer errors
Flexibility in choice of parameters
  Block length, code rate

## Slide 44: Reed-Solomon Codes
Subclass of non-binary BCH codes
Data processed in chunks of m bits, called symbols
An (n, k) RS code has parameters:
  Symbol length: m bits per symbol
  Block length: n = 2m – 1 symbols = m(2m – 1) bits
  Data length: k symbols
  Size of check code: n – k = 2t symbols = m(2t) bits
  Minimum distance: dmin = 2t + 1 symbols

## Slide 45: Block Interleaving
Used to spread errors for detection/correction
  A burst error that may occur is spread out over a number of blocks, making error correction possible
Data written to and read from memory in different orders
Data bits and corresponding check bits are interspersed with bits from other blocks
At receiver, data are deinterleaved to recover original order

## Slide 46: Block Interleaving Illustration

## Slide 47: Error Control Requirements
Error detection
  Receiver detects errors and discards PDUs
Positive acknowledgement
  Destination returns acknowledgment of received, error-free PDUs
Retransmission after timeout
  Source retransmits unacknowledged PDU
Negative acknowledgement and retransmission
  Destination returns negative acknowledgment to PDUs in error