## Slide 1: Chapter 7: Satellite Communications

## Slide 2: History of satellite communication
1945 Arthur C. Clarke publishes an essay about “Extra Terrestrial Relays”
1957 first satellite SPUTNIK
1960 first reflecting communication satellite ECHO
1963 first geostationary satellite SYNCOM
1965 first commercial geostationary satellite: 240 duplex telephone channels or 1 TV channel, 1.5 years lifetime
1976 three MARISAT satellites for maritime communication
1982 first mobile satellite telephone system INMARSAT-A
1988 first satellite system for mobile phones and data communication INMARSAT-C
1993 first digital satellite telephone system
1998 global satellite systems for small mobile phones
2008 GlobalStar has 315,000 subscribers
2015 Iridium orbits (though smaller number of satellites)

## Slide 3: Applications
Traditionally
  weather satellites
  radio and TV broadcast satellites
  military satellites
  satellites for navigation and localization (e.g., GPS)
Telecommunication
  global telephone connections
  backbone for global networks
  connections for communication in remote places or underdeveloped areas
  global mobile communication
 satellite systems to extend cellular phone systems to hard to reach regions.

## Slide 4: Typical satellite systems
base station
or gateway
Inter Satellite Link (ISL)
Mobile User Link (MUL)
Gateway Link (GWL)
footprint
small cells (spotbeams)
User data
PSTN
ISDN
GSM
GWL
MUL
PSTN: Public Switched
Telephone Network

## Slide 5: Basics (Physics 101)
Satellites in circular orbits
  attractive force Fg = m g (R/r)²
  centrifugal force Fc = m r ²
  m: mass of the satellite
  R: radius of the earth (R = 6370 km)
  r: distance to the center of the earth
  g: acceleration of gravity (g = 9.81 m/s²)
  : angular velocity
    ( = 2  f, f: rotation frequency)
Stable orbit
  Fg = Fc

## Slide 6: Satellite period and orbits
10
20
30
40 x106 m
24
20
16
12
8
4
radius
satellite
period [h]
velocity [ x1000 km/h]
synchronous distance
35,786 km

## Slide 7: Basics
elliptical or circular orbits
complete rotation time depends on distance satellite-earth
inclination: angle between orbit and equator
elevation: angle between satellite and horizon
LOS (Line of Sight) to the satellite necessary for connection
   high elevation needed, less absorption due to e.g. buildings
Uplink: connection base station - satellite
Downlink: connection satellite - base station
typically separated frequencies for uplink and downlink
  transponder used for sending/receiving and shifting of frequencies
  transparent transponder: only shift of frequencies
  regenerative transponder: additionally signal regeneration

## Slide 8: Inclination
inclination d
d
satellite orbit
perigee
plane of satellite orbit
equatorial plane

## Slide 9: Elevation
Elevation:
angle e between center of satellite beam
and surface
e
minimal elevation:
elevation needed at least
to communicate with the satellite
footprint

## Slide 10: Link budget of satellites
Parameters like attenuation or received power determined by four parameters:
  sending power
  gain of sending antenna
  distance between sender and receiver
  gain of receiving antenna
Problems
  varying strength of received signal due to multipath propagation
  interruptions due to shadowing of signal (no LOS)
Possible solutions
  Link Margin to eliminate variations in signal strength
  satellite diversity (usage of several visible satellites at the same time) helps to use less sending power
L: Loss
f: carrier frequency
r: distance
c: speed of light

## Slide 11: Atmospheric attenuation
Example: satellite systems at 4-6 GHz
elevation of the satellite
5°
10°
20°
30°
40°
50°
Attenuation of
the signal in %
10
20
30
40
50
rain absorption
fog absorption
atmospheric absorption
e

## Slide 12: Four Different Orbits
Four different types of satellite orbits can be identified depending on the shape and diameter of the orbit:
  GEO: geostationary orbit, ca. 36000 km above earth surface
  LEO (Low Earth Orbit): ca. 500 - 1500 km
  MEO (Medium Earth Orbit) or ICO (Intermediate Circular Orbit): ca. 6000 - 20000 km
  HEO (Highly Elliptical Orbit) elliptical orbits

## Slide 13: Orbit Illustration
earth
km
35768
10000
1000
LEO (Globalstar, Irdium)
HEO
inner and outer Van
Allen belts
MEO (ICO)
GEO (Inmarsat)
Van-Allen-Belts:
ionized particles
2000 - 6000 km and
15000 - 30000 km
above earth surface

## Slide 14: Geostationary satellites
Orbit 35.786 km distance to earth surface, orbit in equatorial plane (inclination 0°)
complete rotation exactly one day, satellite is synchronous to earth rotation
  fix antenna positions, no adjusting necessary
  satellites typically have a large footprint (up to 34% of earth surface!), therefore difficult to reuse frequencies
  bad elevations in areas with latitude above 60° due to fixed position above the equator
  high transmit power needed
  high latency due to long distance (~275 msec)
not useful for global coverage for small mobile phones and data transmission, typically used for radio and TV transmission

## Slide 15: LEO systems
Orbit ca. 500 - 1500 km above earth surface
  visibility of a satellite ca. 10 - 40 minutes
  global radio coverage possible
  latency comparable with terrestrial long-distance connections, ~5 - 10 ms
  smaller footprints, better frequency reuse
  but now handover necessary from one satellite to another
  many satellites necessary for global coverage
  more complex systems due to moving satellites
Examples:
  Iridium (start 1998, 66 satellites)
  Globalstar (start 1999, 48 satellites)

## Slide 16: MEO systems
Orbit ca. 5000 - 12000 km above earth surface
comparison with LEO systems:
  slower moving satellites
  fewer satellites needed
  simpler system design
  for many connections no hand-over needed
  higher latency, ca. 70 - 80 ms
  higher sending power needed
  special antennas for small footprints needed
Example:
  ICO (Intermediate Circular Orbit, Inmarsat) start ca. 2000

## Slide 17: Routing
One solution: inter satellite links (ISL)
  reduced number of gateways needed
  forward connections or data packets within the satellite network as long as possible
  only one uplink and one downlink per direction needed for the connection of two mobile phones
Problems:
  more complex focussing of antennas between satellites
  high system complexity due to moving routers
  higher fuel consumption
  thus shorter lifetime
Iridium and Teledesic planned with ISL
Other systems use gateways and additionally terrestrial networks

## Slide 18: Localization of mobile stations
Mechanisms similar to GSM
Gateways maintain registers with user data
  HLR (Home Location Register): static user data
  VLR (Visitor Location Register): (last known) location of the mobile station
  SUMR (Satellite User Mapping Register):
    satellite assigned to a mobile station
    positions of all satellites
Registration of mobile stations
  Localization of the mobile station via the satellite’s position
  requesting user data from HLR
  updating VLR and SUMR
Calling a mobile station
  localization using HLR/VLR similar to GSM
  connection setup using the appropriate satellite

## Slide 19: Handover in satellite systems
Satellite systems encounter several new situations for handover
  Movements of satellites
  Mobile phone movements as compared to satellite movements

## Slide 20: Handover in satellite systems
Intra satellite handover
  handover from one spot beam to another
  mobile station still in the footprint of the satellite, but in another cell
Inter satellite handover
  handover from one satellite to another satellite
  mobile station leaves the footprint of one satellite
Gateway handover
  Handover from one gateway to another
  mobile station still in the footprint of a satellite, but gateway leaves the footprint
Inter system handover
  Handover from the satellite network to a terrestrial cellular network
  mobile station can reach a terrestrial network again which might be cheaper, has a lower latency etc.

## Slide 21: Overview of LEO/MEO systems

## Slide 22: Constellations
3D-view and top-view

## Slide 23: Starlink
Initial plan was to have 4,000 satellites
  12,000 or 30,000 possible.
  Key is SpaceX Falcon rocket
  Overall, about 2,000 satellites are orbiting the earth.
Satellite details
  500 lb
  Size of a table
  LEO, lower than 600km
Internet provision to low coverage areas
Issues:
  Finance
  Debris
https://satellitemap.space